## Slide 1
BD95841MUVEVK-101 Measurement Report
March 10th, 2014
Hosted by: Xuan Dang

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A)
Multimeter:
  Fluke 87V True RMS
  Fluke 106
Oscilloscope
  Rigol DS1102E
Electronic Load
  B&K BK8500
Current probe
  RP1001C

## Slide 3
Functional Test
Testing procedure
  Connect DC Supply to: [+]VIN(TP1) and [-]GND(TP3) when EN is off. Set output of DC Supply in range from 7.5V to 15V and turn it on.
  Connect Electronic Load to: [+]VOUT(TP2) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 4A and turn on load.
  Move J1 header to turn EN on.
Result:
VIN = 7.5V ~ 15V
IOUT = 4A
VOUT = 3.265V ~ 3.317V. Test passed.

## Slide 4
Hot Plugging Test
Test condition
  VIN = 15V
  IOUT = 4A
  With original diode D1: SMAJ12A
Result:
IIN MAX= 86.4A
VIN peak transient voltage is 17.6V > VIN Maximum Rating (15.2V)
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 5
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-15V
  With SMAJ12A and LED
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15
ICC With SMAJ12A | 0 | 0.0007 | 0.0025 | 0.0054 | 0.0276 | 0.102 | 0.351 | 0.6 | 0.81 | 0.95 | 1.096 | 1.241 | 5.25 | 15.58 | 16.27 | 16.56 | 16.77 | 16.93 | 17.05 | 17.14 | 17.2 | 17.25 | 17.27 | 17.28 | 17.26 | 17.21 | 17.15 | 17.09 | 36.5 | 96 | 160

## Slide 6
Efficiency Measurements
Test condition
  VIN = 12V
  VOUT = 3.3V
  With SMAJ12A and LED
  Room temperature 25oC
Chart: IOUT (mA)
| 0 | 250 | 500 | 750 | 1000 | 1250 | 1500 | 1750 | 2000 | 2250 | 2500 | 2750 | 3000 | 3250 | 3500 | 3750 | 4000
With SMAJ12A, LED | 0 | 79.3 | 86.7 | 87.5 | 89.1 | 89.3 | 89.5 | 89.5 | 89.2 | 89 | 88.7 | 88.3 | 87.9 | 87.4 | 86.8 | 86.3 | 85.7

## Slide 7
Load Response Measurements
Load response characteristic
(VIN=12V, VOUT=3.3V, IOUT=0  4A)
VOUT 50mV/Div. (AC)
IOUT 2A/Div. (DC)

## Slide 8
Load Response Measurements (cont.)
Load response characteristic
(VIN=12V, VOUT=3.3V, IOUT=4A  0)
VOUT 50mV/Div. (AC)
IOUT 2A/Div. (DC)

## Slide 9
Ripple Response Measurements
VOUT Ripple voltage
(VIN=12V, VOUT=3.3V, IOUT=4A)
VSW 5V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 10
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=12V, VOUT=3.3V, IOUT=0A)
VSW 5V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 11
Input Voltage Ripple Measurements
VIN Ripple voltage
(VIN=12V, VOUT=3.3V, CIN=10uF (x2)+ 0.1uF, IOUT=0A)
VIN 20mV/Div. (AC)

## Slide 12
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=12V, VOUT=3.3V, CIN=10uF (x2)+ 0.1uF, IOUT=4A)
VIN 50mV/Div. (AC)